## Slide 1: Outlier Detection in Condition Monitoring
Master Thesis
Ralph Fehrer
„Intelligente Eingebettete Mikrosysteme“
2012-2013

## Slide 2: Overview
  Condition Monitoring
  Feature Extraction Methods
  One Class Classification
  Experiments
  Summary
  Outlook

## Slide 3
Condition Monitoring

## Slide 4: Condition Monitoring
„Condition Monitoring is a process
of monitoring a system
by studying certain selected parameters
in such a way,
that significant changes of those parameters
are related to developing failures“
Artur G. O. Musambara , Harare 2012

## Slide 5: Condition Monitoring
Benefits of (computerized) Condition Monitoring
Predictive maintenance approach, based on machine conditions
Prevention of machine failure
Lifetime prediction
Overall reduction of operating costs

## Slide 6: Condition Monitoring Framework
Marwala, 2012
Feature extraction (Fourier, Short Time Fourier, Wavelet Transform…)
Selection of most significant features
(PCA…)
Classification / Outlier detection
(Machine Learning/Pattern Recognition)
Lifetime prediction, maintenance scheduling…
Sensors atttached to monitored system (accelerometers, thermometers…)

## Slide 7: Condition Monitoring Framework
Marwala, 2012
Focus of this Thesis

## Slide 8
Data Analysis Feature Extraction

## Slide 9: Data Analysis / Feature Extraction
  Mel Frequency Cepstral Coefficients (MFCC)
  Higuchi Fractal Dimensions (HFD)
  Kurtosis

## Slide 10: Mel Frequency Cepstral Coefficients
Basics
Cepstrum:
LTI:
Cepstrum(LTI):
Ceptstrum separates signal
from transmission path characteristics

## Slide 11: Mel Frequency Cepstral Coefficients
MFCC feature extraction method
Short Time Fourier Transform (STFT) of time signal
transformation into time frequency domain
Mel transform of frequency spectrum
adaption to frequency response of human
auditory system
Transformation of logarithmic frequency spectrum to time domain through Discrete Cosine Transform

## Slide 12: Fractal Dimensions
FD in time signal analysis
Measure for the irregularity of signal shape
Fractal dimensions of a signal are in the range between 1 and 2
Several methods exist, usually measuring length at different scales
Higuchi algorithm implemented for this thesis (Matlab)

## Slide 13: Fractal sample
Weierstraß function with known fractal dimension
used to validate Higuchi algorithm

## Slide 14: Higuchi Fractal Dimensions
Algorithm
Creation of k new signals from the time signal at different scales
Measuring of the length of the scaled time signals, i.e. of the distance between points
Calculation of HFD through the relation

## Slide 15: Kurtosis
Measure of curve „peakedness“
Normalized order moment:

## Slide 16
Decision Making Classification

## Slide 17: Classification
Data samples for all classes
Classification function
Training by optimizing through error function, e.g.
Supervised, multi-class

## Slide 18: Classification
Supervised, one-class
Typical Condition Monitoring scenario: Only samples for one class (normal conditions)
Calculation of a closed boundary
Also known as: Data Description, Domain Description, Outlier or Novelty Detection
Target objects
*
*
*
Outlier objects

## Slide 19: One Class Classification
Components
Similarity measure measure for the relation of new data objects to the known target data description
  (distance)
  (probability)
Threshold

## Slide 20: One Class Classification
Classifier functions
Where is the indicator function s.t.
1=target, 0=outlier

## Slide 21: Support Vector Data Description
Principle: Support objects defining a hypersphere with radius
R and center a
Training: Minimization of R such that most traning target objects are inside hypersphere
Classification: new objects are target objects if they are inside the
boundary, outliers otherwise

## Slide 22: K-Center Data Description
Principle: K support objects surrounded by Receptive Fields of equal radius R, data objects belong to the receptive fields of the nearest support object
Training: Selection of support objects such that R is minimal and all sample objects are inside receptive fields
Classification: new objects are target objects if their distance to the nearest support object is smaller than the threshold

## Slide 23: K-Means Data Description
Principle: K clusters, data objects belong to the clusters of the nearest cluster center
Training: recalculation of cluster centers as means of objects in the cluster until convergence
Classification: new objects are target objects if their distance to the nearest cluster center is smaller than the predefined threshold

## Slide 24: Nearest Neighbor Data Description
Principle: Distances between nearest data objects
Training: No training required
Classification: new objects are target objects if their distance to the nearest sample target object is smaller than the
distance of the nearest target object to its nearest neighbor

## Slide 25: Parzen Window Data Description
Principle: Density measure based on accumulation of distances between a data object and the sample target objects
Training: No training required
Classification: new objects are target objects if their density
is above a predefined threshold, outliers otherwise

## Slide 26: SOM Data Description
Principle: prototypes of sample target objects , associated with nodes in a grid structure
Training: sequential presentation of sample target objects,
update of nearest prototype and the surrounding
prototypes
Classification: new objects are target objects if their distance to the nearest prototype is below the predefined threshold, outliers otherwise

## Slide 27: Random Forest
Construction of many trees
Proximity Matrix - matrix where entries are measures for the proximity of training objects
Outlier measure – detection of outliers in training set
Feature importance measure
Class centers / prototypes
Unsupervised mode
  All training samples treated as target class data
  Construction of a synthetic second class
  Construction of a 2-class random forest

## Slide 28: Random Forest Data Description
Principle: See above
Training: Random Forest in supervised mode, calculation of target class center(s) / prototype(s)
Classification: new objects are target objects if their distance to
the (nearest) target class prototype is below a pre-
defined threshold, outliers otherwise
Implemented for this thesis in R and Matlab, Proof of concept in experiment part

## Slide 29
Experiments

## Slide 30: Data Acquisition/Roller Bearing Data
Vibration Data
(accelerometers)

## Slide 31: Data Analysis/Preprocessing
4 vibration signals: 1.normal conditions 2.ball fault conditions 3.inner raceway fault 4.outer raceway fault
Obtained from Case Western University
Split signals into segments
corresponding to 5 revolutions
of Roller Bearing

## Slide 32: Data Analysis/ Data sample
Normal
conditions
Ball fault
conditions
Inner raceway fault
conditions
Outer raceway fault
conditions
1 segment corresponding to 5 revolutions of Roller Bearing

## Slide 33: Data Analysis/Feature Extraction
~450 signal segments
per condition signal
For each segment
Extract n MFCCs
Extract n HFDs
Calculate Kurtosis

## Slide 34: Data Analysis/Feature Extraction
Mel Frequency Cepstral Coefficients
(MFCC) of first segment
Normal condition
Ball fault
Inner raceway fault
Outer raceway fault

## Slide 35: Data Analysis/Feature Extraction
Higuchi Fractal Dimensions
(HFD)

## Slide 36: Data Analysis/Feature Extraction
 |  | … |  |  | … |  | 
Feature Vector 1 | ### | ### | ### | ### | ### | ### | ###
… | ### | ### | ### | ### | ### | ### | ###
Feature Vector N | ### | ### | ### | ### | ### | ### | ###
 |  | … |  |  | … |  | 
Feature Vector 1 | ### | ### | ### | ### | ### | ### | ###
… | ### | ### | ### | ### | ### | ### | ###
Feature Vector N | ### | ### | ### | ### | ### | ### | ###
Feature data set
construction
1 feature data set per condition

## Slide 37: Decision Making/ OC-training
K-Center-dd
K-Means-dd
NN-dd
SV-dd
Parzen-d
SOM-dd
RF-dd
Trained models
Training with normal
features only

## Slide 38: Evaluation/ Outlier Detection
Classification of normal and fault condition
test data

## Slide 39: Evaluation/ Outlier Detection
Training and classification runtimes

## Slide 40: Evaluation/ Feature Reduction
Feature reduction with random forest
variable importance measure

## Slide 41: Conclusions
Altogether good results with the combination of feature extraction methods and one-class- classifiers for the roller bearing dataset
excellent results with the new random forest one class classifier concept
huge differences in training times (not that important in real world applications)
underperformers: SVDD (w.r.t. time and accuracy), Parzen Window (worst classifier)

## Slide 42: Outlook
Application of One-Class-Classifiers in Ensemble Methods (Batch and Ada Boost)
Calculation of several random forest class centers/prototypes representing the target class (based on proximity matrix)
Combination of semi-supervised / one class classification scenarios

## Slide 43: End
Thank You!